## Slide 1: CSM 153 CIRCUIT THEORY
Akwasi Acheampong Aning, PhD
Science & Technology
Kwame Nkrumah University of

## Slide 2: COURSE OUTLINE
Unit 3: Networks Theorems
(a) Superposition Theorem
(b) Thevenin’s Theorem
(c) Norton’s Theorem
(d) Delta and Wye Networks
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 3: Direct Circuit Analysis
In any linear resistive network, the voltage across or the current through any resistor or source may be calculated by adding algebraically all the individual voltages or currents caused by the separate independent sources acting alone, with all other independent voltage sources replaced by short circuits and all other independent current sources replaced by open circuits.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 4: Direct Circuit Analysis
Replace all sources except one by their internal resistances.
Calculate all the currents and voltages for that one source. Note the current directions and terminal polarities
Repeat steps 1 and 2 for each source
Determine the currents by algebraically adding the currents due to each source
Determine the voltages by either algebraically adding the voltages for each source or using the total current and Ohm’s law
Use basic circuit concepts to find other quantities
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 5: Direct Circuit Analysis
Replace all sources except one by their internal resistances.
Calculate all the currents and voltages for that one source. Note the current directions and terminal polarities
Repeat steps 1 and 2 for each source
Determine the currents by algebraically adding the currents due to each source
Determine the voltages by either algebraically adding the voltages for each source or using the total current and Ohm’s law
Use basic circuit concepts to find other quantities
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 6: Direct Circuit Analysis
Example: Use superposition to find the currents, voltages and power in the circuit
Soln
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 7: Direct Circuit Analysis
Soln Cont
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 8: Direct Circuit Analysis
Soln Cont
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 9: Direct Circuit Analysis
Soln Cont
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem

## Slide 10: Direct Circuit Analysis
Soln Cont
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Superposition Theorem
This fig shows the correct directions and polarities
Power is calculated either using the total voltage or the total current

## Slide 11: Direct Circuit Analysis
In circuit theory, Thévenin's theorem for linear electrical networks states that any combination of voltage sources,
current sources, and resistors with two terminals is electrically equivalent to a single voltage source V and a
single series resistor R. For single frequency AC systems the theorem can also be applied to general impedances,
not just resistors.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Thevenin’s Theorem

## Slide 12: Direct Circuit Analysis
Identify the circuit that is to be Théveninized and the load that is connected to it
Disconnect the load from the circuit that is to be Théveninized
Use circuit concepts to find the voltage across the open circuited two terminals. This is ETH
Find the resistance looking into the two terminals with the sources replaced by their internal resistances. This is RTH
Reconnect the load to the Thévenin equivalent and make any required analysis of the load condition
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Thevenin’s Theorem

## Slide 13: Direct Circuit Analysis
Find the power in the 2 Ω resistor R6 using Thevenin's theorem
Soln.
Remove R6 from the circuit
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Thevenin’s Theorem

## Slide 14: Direct Circuit Analysis
Soln Cont.
Redraw the circuit after
finding the resistance,
RA of the parallel branch
R3||R4
Redraw the circuit and calculate the voltage across the break AB which is the voltage across RA = VT. Remember that 20V is dropped across R1 and also across R2+RA.
Since R2 = RA = 5 half of the voltage is dropped across each resistor VT = 10 V
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Thevenin’s Theorem

## Slide 15: Direct Circuit Analysis
Soln Cont.
Remove V1 and replace it with a short circuit
This action also short circuits R1 out of the circuit
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Thevenin’s Theorem

## Slide 16: Direct Circuit Analysis
Soln Cont.
RT = (RAxR2) / (RA+R2) + R5 + R7 = 14.5 Ω
I = VT/(RT + R6) = 10/16.5 = 0.606A
Power dissipated by R6 = I x I x R = 0.73 Watts
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Networks Theorems: Thevenin’s Theorem

## Slide 17: Direct Circuit Analysis
Any two-terminal linear bilateral dc network can be replaced by an equivalent circuit consisting of a current and a parallel resistor.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Norton’s Theorems

## Slide 18: Direct Circuit Analysis
Identify the circuit that is to be Nortonized and the load that is connected to it
Disconnect the load from the circuit that is to be Nortonized
Short circuit the terminals and use circuit concepts to find the short circuit current. This is IN
Open the terminals, replace the sources by their internal resistance and find the resistance looking into the terminals. This is RN
Reconnect the load and make any required analysis
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Norton’s Theorems

## Slide 19: Direct Circuit Analysis
Find the Norton equivalent of the circuit below
Soln
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Norton’s Theorems
ISC = E/R2 =60 V/30 Ω =2 A then, IN = 2 A

## Slide 20: Direct Circuit Analysis
Soln Cont
Replacing E by its Ri a short circuit
also short out R1
So RN = R2 = 30 Ω
This is the Norton’s
equivalent circuit
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Norton’s Theorems

## Slide 21: Direct Circuit Analysis
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Delta and Wye Network

## Slide 22: Direct Circuit Analysis
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Delta and Wye Network

## Slide 23: Direct Circuit Analysis
Conversion from Wye to Delta
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Delta and Wye Network

## Slide 24: Direct Circuit Analysis
Conversion from Wye to Delta
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Network Theorems: Delta and Wye Network

## Slide 25: Merci
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD