## Slide 1: CSM 153 CIRCUIT THEORY
Akwasi Acheampong Aning, PhD
Science & Technology
Kwame Nkrumah University of

## Slide 2: COURSE OUTLINE
Unit 1: Basic Concepts and Elements
Charge and Matter
Force, Energy and Power
Resistor, Capacitor and Inductor
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 3: COURSE OUTLINE
Unit 2: Direct Circuit Analysis
Ohm’s law
Series Circuit
Parallel Circuit
Methods of Analysis
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 4: COURSE OUTLINE
Unit 3: Networks Theorems
(a) Superposition Theorem
(b) Thevenin’s Theorem
(c) Norton’s Theorem
(d) Delta and Wye Networks
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 5: COURSE OUTLINE
Unit 4: AC Circuits
Alternating Currents and Voltages
R, L and C Elements
Power in AC Circuits
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 6: Recommended Textbooks
Giancoli, D. C. (2009). Physics for Scientists and Engineers with Modern Physics (4th Ed.). Pearson Education, Inc.
Circuit Analysis: Theory and Practice. Allan H Robbins and Wilhelm C Miller
Basic Circuit Theory. I. D. Mayergoyz and W. Lawson
Electrical Circuit Theory and Technology. John Bird
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 7: Assessment
Continuous Assessment (Classwork, Homework, Presentation, Mid-Semester and Attendance) = 30
End of Semester Examination (Multiple Choice Questions, Questions and Problems) = 70
Total 30 + 70 = 100
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD

## Slide 8: Basic Concepts and Elements
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter
Atomic Model
A simple model of the atom depicts that it has a tiny heavy positively charged centre, called nucleus.
The nucleus is surrounded by one or more negatively charged particles, called electrons.

## Slide 9: Basic Concepts and Elements
The Structure of the Atom
Sub-atomic particles make up atoms, which make up ordinary matter.
Thus, matter is made up of several sub-atomic particles( protons, electrons and neutrons).
The protons and neutrons (nucleons) are closely packed to form the nucleus.
If the nucleus is considered a sphere, its diameter is of the order of 10 –14m.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 10: Basic Concepts and Elements
The Structure of the Atom
The total charge of electrons balance the total charge of protons.
The atom as a whole is electrically neutral (no charge).
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 11: Basic Concepts and Elements
The Structure of the Atom
The Neutron
It has no electrical charge so it is electrically neutral.
It cannot be deflected by electric and magnetic fields.
They are more penetrating than the electron or the proton.
Reason: Since it has no charge, it is not affected by the electric and magnetic fields around electrons and nuclei.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 12: Basic Concepts and Elements
The Structure of the Atom
The Electron
The electron has negative charge of 1.6 x 10 –19 coulomb (C).
It can be deflected by electric and magnetic fields.
It is always deflected towards the positive plate in an electric field.
Reason: Students give reason
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 13: Basic Concepts and Elements
The Structure of the Atom
The Electron
The electron has negative charge of 1.6 x 10 –19 coulomb (C).
It can be deflected by electric and magnetic fields.
It is always deflected towards the positive plate in an electric field.
Reason: Students give reason
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 14: Basic Concepts and Elements
The Structure of the Atom
The Proton
It has a positive charge equal in magnitude to the charge on the electron.
It can be deflected by electric and magnetic fields.
It is always deflected towards the negative plate in an electric field.
Reason: Students give reason.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 15: Basic Concepts and Elements
Matter is made up of atoms, which are in turn composed of electrons, protons, and neutrons.
The protons and neutrons of an atom share a very small volume of space called the nucleus of the atom.
The electrons are attracted to the nucleus by a force called the electrostatic force or Coulomb force.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 16: Basic Concepts and Elements
This force exists because the electrons and nuclei have electric charges of opposite sign.
The electron is negatively charged and the nucleus is positively charged.
The positive charge of the nucleus is entirely due to the charges of protons, since the neutrons do not have any net electric charge
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 17: Basic Concepts and Elements
The charge of an object can be regarded as the algebraic sum of all the elementary atomic charges which make up the object.
The electric charge is an intrinsic property of the elementary particles, such as electron or proton, just as mass is an intrinsic property of matter.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 18: Basic Concepts and Elements
Thus, electric charge is a property (characteristic) associated with fundamental particles wherever they exist.
Mass can create a gravitational field g, which in turn can exert a force mg on a body of mass m.
Thus, mass m can create gravitational force Fg = mg.
Electric charge, like mass, is an important inherent property of matter which can be present in both large and small bodies.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 19: Basic Concepts and Elements
Electric charge q can create electric field E in space, which can also exert a force qE on another body of charge q.
Thus, electric charge q can create electric or electrostatic force FE = qE.
These fields in turn transmit forces to other charged bodies and thereby affect their motion.
Therefore, the region in space around the charged body, where electric forces can be experienced defines electric field.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 20: Basic Concepts and Elements
Since charge is a fundamental property of matter (like mass) it needs a unit.
A natural unit would be e, the charge of the electron. The SI unit is the Coulomb (C)
|e| = 1.60219 x 10-19 C (i.e. 1C = 6.2 x 1018 |e|)
Any charge q, occurring in nature can be expressed as
where N is an integer and e = 1.6x10-19C
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 21: Basic Concepts and Elements
Electric charge is thus said to be quantised and exists only in discrete amounts (values) such as +1e, +2e, +3e, etc.
For example the cations Na+, Mg2+ and Al3+ have charges +e, +2e and +3e respectively.
Thus the magnitude of these charges on the cations are 1.6x10-19C, 3.2x10-19C and 4.8x10-19C respectively.
Similarly charges on Cl- and SO4-2 have values of
-1.6x10-19C and -3.2x10-19C respectively
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 22: Basic Concepts and Elements
Another important feature of charge is that electric charge is always conserved
In any interaction or reaction, the initial and final values of the total electric charge must be the same.
Thus, total electric charge is neither created nor is it destroyed.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 23: Basic Concepts and Elements
Matter or solid state materials may be classified into insulators, semiconductors and conductors.
Insulators:
From atomic point of view electrons in insulators are firmly (tightly) bound to the nucleus.
Thus unable to move under applied potential difference for electrical conduction.
Therefore, electrical conduction in insulators is by the mechanism of dielectric conduction.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 24: Basic Concepts and Elements
Semiconductors:
Electrons in semiconductors are relatively not firmly (tightly) bound to the nucleus.
Thus only few electrons are able to move under applied potential difference for electrical conduction.
However, electrons can be generated to take part in electronic semi-conduction.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 25: Basic Concepts and Elements
Conductors:
In metallic conducting materials some of the electrons are very loosely bound to the nucleus.
Thus electrons can move about freely within the crystal structure.
Such electrons are called free electrons or conduction electrons.
Therefore, electric current through metals is by electronic conduction.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Charge and Matter

## Slide 26: Basic Concepts and Elements
Force:
The electrical force between two stationary charged particles is given by Coulomb’s Law.
The force is:
directly proportional to the product of the charges, q1 and q2, on the two particles.
inversely proportional to the square of the separation, r between the particles and directed along the line joining them.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 27: Basic Concepts and Elements
Force:
The force is attractive if the charges are of opposite sign.
The force is repulsive if the charges are of like sign
The force is a conservative force.
What is a conservative force? Students discuss.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 28: Basic Concepts and Elements
Force:
Coulomb’s Law, Equation
Mathematically,
The SI unit of charge is the coulomb (C)
ke is called the Coulomb constant
  ke =1/4πƐo = 8.9875 x 109 N.m2/C2
  Ɛo is the permittivity of free space
  Ɛo = 8.8542 x 10-12 C2 / N.m2
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 29: Basic Concepts and Elements
Force:
Coulomb’s Law, Equation
It is directed along the line joining centres of two particles.
It is proportional to the product of the magnitude of the two charges.
It is inversely proportional to the square of the separation or distance, r between two charges.
4. The force is attractive if charges are opposite in sign
and repulsive if charges have the same sign.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 30: Basic Concepts and Elements
Force:
Coulomb’s Law, Equation
The electrical force between the electron and proton is found from Coulomb’s law
  using
This can be compared with the gravitational force between the electron and the proton given by
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 31: Basic Concepts and Elements
Potential:
Electric potential V at a point in an electric field is defined as the potential energy per unit charge. i.e.
Similarly, electric potential can be defined as the work done per unit charge in moving the charge from infinity to the point.
ie
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 32: Basic Concepts and Elements
Potential:
Potential is a scalar quantity, and not a vector with S.I. unit Joule per Coulomb [JC-1 or Volt(V)].
The potential can be positive, negative or zero depending on the signs and magnitude of q and
The potential energy per unit charge (potential) is independent of the charge q of the particle we use.
The potential is characteristic only of the electric field we are investigating.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 33: Basic Concepts and Elements
Potential:
The electric potential difference ΔV between any two points i and f in an electric field is equal to the difference in potential energy per unit charge between the two points.
i.e.
Thus, we have
Therefore, potential difference between two points is the negative of the work done by the electrostatic force to move a unit charge from one point to the other in the field.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 34: Basic Concepts and Elements
Potential:
Consider a unit positive test charge q0 moved from infinity to a point at a distance x in the electric field of the charge q.
Then electric force F on the test charge is given by
F = q0E ----- (1)
Thus, F = E since q0 is a unit charge.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power
Dx
r
q0
¥
q
P
E

## Slide 35: Basic Concepts and Elements
Potential:
Then the work done DW in moving the unit charge through a small distance Dx toward the charge is given by DW = F(-Dx) .
i.e. dW = - Fdx = - Edx
But
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 36: Basic Concepts and Elements
Potential:
But the potential, V is equal to the work done per unit test charge, W/q0.
Therefore,
NB:
A positively charged particle produces a positive electric potential.
A negatively charged particle produces a negative electric potential.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 37: Basic Concepts and Elements
Potential:
When dealing with energies of electrons, molecules or atoms, the joule appears to be a very large unit of energy.
For this reason alternative unit of energy called the Electronvolt (eV) is used.
Electronvolt is defined as the energy gained by an electron accelerated through a potential difference of one volt (1V).
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 38: Basic Concepts and Elements
Potential:
Therefore, the electronvolt is the energy that can be acquired by a particle, which carries a charge of the magnitude of the charge on the electron (q=e) and moved through a potential difference of 1V.
But e = 1.6x10-19 C and change in potential energy is qV or eV= (1.6x10-19Cx1.0V) J
Hence 1eV = 1.6x10-19 J.
NB: The electronvolt is not SI unit, however it is useful in stating the energies of atoms, molecules and elementary particles.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 39: Basic Concepts and Elements
Current:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power
The electric field exerts forces on the conduction electrons, causing them to be accelerated.
Hence the electrons move and an electric current is established.
After a very short time, the flow of the electrons reaches a constant value and the current is said to be in a steady state.
When a battery or source of emf is connected to a wire made into a loop, electric field is set up inside the material of the wire.

## Slide 40: Basic Concepts and Elements
Current:
If charges (conduction electrons) dQ flow past a section (hypothetical plane) of a conductor in a time dt, then the current I through that section is defined as
The total charge Q that passes through the section of the conductor in a time interval from 0 to t is given by
\ Q = It
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power
SI unit for current is coulomb per second or ampere (A).

## Slide 41: Basic Concepts and Elements
Current:
Electrical conduction in a wire (metal) is due to the movement of free electrons.
Emf set up an electric field in the metal.
The electron are then accelerated by the field and they gain velocity and energy.
The moving electrons collide with atoms of the metal vibrating about their fixed mean position and give up some of their energy to the atoms.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 42: Basic Concepts and Elements
Current:
The amplitude of vibrations of the atoms increases and the temperature of the metal rises.
However, on the average the electrons drift in the opposite direction to the electric field with a mean speed.
Therefore the drift constitute electric current.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 43: Basic Concepts and Elements
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 44: Basic Concepts and Elements
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 45: Basic Concepts and Elements
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Force, Energy and Power

## Slide 46: Basic Concepts and Elements
Resistor:
Resistors are specifically designed to possess resistance and are used in almost all electronic and electrical circuits.
Resistors are the simplest components in any circuit but their effect is very important in determining the operation of a circuit
Resistance is represented by the symbol R and is measured in units of ohms (after Georg Simon Ohm). The symbol for ohms is the capital Greek letter omega (Ω).
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 47: Basic Concepts and Elements
Resistor:
The resistance of a material is dependent upon several factors:
Type of material
Length of the conductor
Cross-sectional area
Temperature
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 48: Basic Concepts and Elements
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 49: Basic Concepts and Elements
Resistor:
Resistivity of conductors
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 50: Basic Concepts and Elements
Resistor:
There are two main types of resistors:
Fixed Resistors are resistors with constant resistance values and
Variable resistors are three terminal resistors are used to adjust the volume of our radios, set the level of lighting in our homes, and adjust the heat of our stoves and furnaces
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 51: Basic Concepts and Elements
Resistor:
Large resistors have their resistor values and tolerances printed on their cases.
Smaller resistors are too small to have their values printed on the component.
They are usually covered by an epoxy or similar insulating coating
over which several coloured bands are printed radially
The coloured bands provide a quickly recognizable code for determining the value of resistance, the tolerance (in percentage), and occasionally the expected reliability of the resistor.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 52: Basic Concepts and Elements
Resistor:
The coloured bands are always read from left to right, left being defined as the side of the resistor with the band nearest to it.
The first two bands represent the first and second digits of the resistance value.
The third band is called the multiplier band and represents the number of zeros following the first two digits; it is usually given as a power of ten.
The fourth band indicates the tolerance of the resistor, and the fifth band (if present) is an indication of the expected reliability of the component.
The reliability is a statistical indication of the expected number of components that will no longer have the indicated resistance value after 1000 hours of use.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 53: Basic Concepts and Elements
Resistor:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 54: Basic Concepts and Elements
Resistor:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 55: Basic Concepts and Elements
Resistor:
Fixed resistor Variable resistor
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 56: Basic Concepts and Elements
Capacitor:
A capacitor is an electrical device that is used to store electrical energy.
Next to the resistor, the capacitor is the most commonly encountered component in electrical circuits.
Capacitors are used extensively in electrical and electronic circuits.
Uses of Capacitors
To smooth rectified ac outputs
In telecommunication equipment – such as radio receivers – for tuning to the required frequency
In time delay circuits
In electrical filters
in oscillator circuits and
in magnetic resonance imaging (MRI) in medical body scanners
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 57: Basic Concepts and Elements
Capacitor:
Capacitance is the electrical property of capacitors: it is a measure of how much charge a capacitor can hold
A capacitor consists of two conductors separated by an insulator. One of its basic forms is the parallel-plate capacitor
It consists of two metal plates separated by a non-conducting material (i.e., an insulator) called a dielectric.
The dielectric may be air, oil, mica, plastic, ceramic, or other suitable insulating material.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 58: Basic Concepts and Elements
Capacitor:
Picture of capacitors
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 59: Basic Concepts and Elements
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 60: Basic Concepts and Elements
Capacitor:
For a parallel-plate capacitor, capacitance C is defined as the ratio of charge on each (either) plate to the potential difference between the plates
The capacitance of a parallel plate capacitor is:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
C increases as we increase the area A or decrease separation d of the plates.
Resistor, Capacitor and Inductor

## Slide 61: Basic Concepts and Elements
Capacitor:
For a Parallel Plate Capacitor, the capacitance depends only on the following factors:
Area (Geometry) of the plates.
Separation (distance) between the plates.
The nature of material (dielectric material) between the plates.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 62: Basic Concepts and Elements
Capacitor:
For an isolated sphere, the capacitance is:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
C is independent of the charge on the spherical conductor but depends only on the radius R.
Resistor, Capacitor and Inductor

## Slide 63: Basic Concepts and Elements
Inductor:
Inductance is due entirely to the magnetic field created by the current, and its effect is to slow the build-up and collapse of the current and—in general—oppose its change
A component called an inductor is used when the property of inductance is required in a circuit.
The basic form of an inductor is simply a coil of wire.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 64: Basic Concepts and Elements
Inductor:
Factors which affect the inductance of an inductor include:
the number of turns of wire – the more turns the higher the inductance
the cross-sectional area of the coil of wire – the greater the cross-sectional area the higher the inductance
the presence of a magnetic core – when the coil is wound on an iron core the same current sets up a more concentrated magnetic field and the inductance is increased
the way the turns are arranged – a short, thick coil of wire has a higher inductance than a long, thin one.
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 65: Basic Concepts and Elements
Inductor:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor

## Slide 66: Basic Concepts and Elements
Symbols:
www.knust.edu.gh
CSM 153 Circuit Theory
Akwasi Acheampong Aning, PhD
Resistor, Capacitor and Inductor