## Slide 1: PHY 251 Electronics I CSM251 Introductory Electronics
Prof. Francis Kofi Ampong
Department of Physics
KNUST
Kofi’s workbench

## Slide 2: Polite Request: If You Have A Mobile Phone Please Switch It Off Please Do Not Send Or Receive Texts During This Lecture Thank You!

## Slide 3: Textbooks
Microelectronic circuits ------(Engineering library) By Sedra and Smith 3rd or higher editions
The Science of Electronics Analog Devices By Thomas L. Floyd David M. Buchla

## Slide 4: Text book for digital electronics

## Slide 5
Course Structure: Lecture sessions , Assignments and Exams
Attendance 5 %
Assignments 5 %
Mid Sem Exam 20 %
End of Sem Exam 70%

## Slide 6
Course Objective:
To develop a background knowledge of semiconductor theory sufficient to understand modern semiconductor devices.

## Slide 7: Outline of syllabus for CSM/PHY 251
1.1 Basic Semiconductor physics
1.2 The pn Junction
1.3 Analysis of diode circuits
1.4 Applications of diode circuits
1.5 The bipolar junction transistor (BJT) – analysis and applications
1.6 MOSFETs
1.7 Operational Amplifiers

## Slide 8: Introduction: What are Semiconductor devices?
Semiconductor devices are electronic components that exploit the electronic properties of semiconductor materials, principally silicon, and germanium.

## Slide 9: Why are we interested in Semiconductor devices?
In the early days of radio and television, transmitting and receiving equipment relied on vacuum tubes, but these have been completely replaced in the last three decades by
semiconductor devices, which include transistors, diodes, relays integrated circuits and other electronic components.

## Slide 10
To understand how diodes, transistors and integrated circuits work, you first have to study semiconductors: materials that are neither conductors nor insulators.
Semiconductor devices, such as transistors and diodes, form the basis of nearly all modern electronic systems.

## Slide 11: More Reasons
Semiconductor devices are the foundation of the electronic industry, which is the largest industry in the world with global sales over one trillion dollars since 1998.
A basic knowledge of semiconductor devices is essential to understanding of advanced courses in electronics.

## Slide 13
Semiconductor devices serve as the heart of microelectronics.

## Slide 14: LECTURE 1: Semiconductors Basics
PHY 251
Electronic I

## Slide 15: Introduction
IN THIS LECTURE WE WILL LEARN:
  The basic properties of semiconductors and, in particular, silicone – the material used to make most modern electronic circuits.
  How doping a pure silicon crystal dramatically changes its electrical conductivity – the fundamental idea in underlying the use of semiconductors in the implementation of electronic devices.

## Slide 16: From discrete energy levels to energy bands

## Slide 17: Review of Basic Atomic Model
Atoms are comprised of electrons, neutrons, and protons.
Electrons are found orbiting the nucleus of an at atom at specific intervals, based upon their energy levels.
The outermost orbit is the valence orbit.

## Slide 18
From discrete energy levels to energy bands: - atoms have discrete energy levels which are widely spaced.
  The electrons can only be found in these energy states

## Slide 19: From discrete energy levels to energy bands
valence electron – is an electron that participates in the formation of chemical bonds.
  Atoms with one or two valence electrons more than a closed shell are highly reactive because the extra electrons are easily removed to form positive ions.
covalent bond – is a form of chemical bond in which two atoms share a pair of electrons.
  It is a stable balance of attractive and repulsive forces between atoms when they share electrons.

## Slide 20: Isolated Semiconductor Atoms
Silicon and Germanium are electrically neutral; that is, each has the same number of orbiting electrons as protons.
Both silicon and germanium have four valence band electrons, and so they are referred to as tetravalent atoms. This is an important characteristic of semiconductor atoms.

## Slide 21: Silicon Covalent Bond Model (cont.)
Silicon atom
Silicon atom
Covalent bond
Silicon has four electrons in the outer shell.
Single crystal material is formed by the covalent bonding of each silicon atom with its four nearest neighbors.

## Slide 22: Silicon Covalent Bond Model (cont.)
Silicon atom
Covalent bonds in silicon
On the average, each silicon atom will have eight electrons in its outermost shell

## Slide 23: Silicon Covalent Bond Model (cont.)

## Slide 25: Conduction in materials
What is crucial to the conduction process is the availability of free electrons.
That is before a material can conduct electric current it must have some electrons which can move freely inside the material.
In silicon the bonding process uses up all the available electrons, so at absolute zero temperature, there are no electrons available for conduction.

## Slide 26
Si
Si
Si
Si
Si
Si
Si
Si
Si
At finite temperatures however, the atoms vibrate randomly, having occasionally much more than the average thermal energy

## Slide 27
Si
Si
Si
Si
Si
Si
Si
Si
Si
At certain instants at certain atoms there is there is enough energy to break the covalent bond and liberate an electron. Once liberated, they wander aimlessly through the crystal, and are said to be in the conduction band, where they can contribute to electric current. Those electrons which still remain bound are said to be in the valence band

## Slide 29: So what can we say about this?
We may say that all the electrons are in the valence band at 0oK (that is all electrons remain bound to their parent atom).
There is an energy gap above the valence band before the conduction band starts.
This means that for an electron to be in the conduction band; that is, to get an electron in a state in which it can take up kinetic energy from an electric field and can contribute to an electric current, we first have to give it a package of energy.
This can come from thermal excitation, or by photon excitation quite independently of temperature

## Slide 30: 3.1: Intrinsic Semiconductors
silicon at low temps:
  all covalent bonds are intact
  no electrons are available for conduction
  conducitivity is zero
silicon at room temp:
  sufficient thermal energy exists to break some covalent bonds, freeing an electron and creating hole
  a free electron may wander from its parent atom
  a hole will attract neighboring electrons
the process of freeing electrons, creating holes, and filling them facilitates current flow
Figure 3.2: At room temperature, some of the covalent bonds are broken by thermal generation. Each broken bond gives rise to a free electron and a hole, both of which become available for current conduction.

## Slide 31: Questions ?
Can you think of a device that generates free electrons when external energy such as light is applied to it?

## Slide 33: Energy-band Diagram
A very important concept in the study of semiconductors is the energy-band diagram
It is used to represent the range of energy a valence electron can have
For semiconductors the electrons can have any one value of a continuous range of energy levels while they occupy the valence shell of the atom
  That band of energy levels is called the valence band
Within the same valence shell, but at a slightly higher energy level, is yet another band of continuously variable, allowed energy levels
  This is the conduction band

## Slide 34: Energy-band diagram – classification of materials
Conduction Band
Valence Band
Conduction Band
Energy Gap
Valence Band
Conduction Band
Energy Gap
Valence Band
Conduction Band
Insulator
Semiconductor
Conductor
Conductor
Empty allowed energy band
Full allowed energy band

## Slide 35: Band Gap
Between the valence and the conduction band is a range of energy levels where there are no allowed states for an electron
This is the band gap
In silicon at room temperature [in electron volts]:
Electron volt is an atomic measurement unit, 1 eV energy is necessary to decrease of the potential of the electron with 1 V.

## Slide 36: Insulators, Semiconductors, and Metals
This separation of the valence and conduction bands determines the electrical properties of the material
Insulators have a large energy gap
  electrons can’t jump from valence to conduction bands
  no current flows
Conductors (metals) have a very small (or nonexistent) energy gap
  electrons easily jump to conduction bands due to thermal excitation
  current flows easily
Semiconductors have a moderate energy gap
  only a few electrons can jump to the conduction band
    leaving “holes”
  only a little current can flow

## Slide 37: Semiconductor Energy Band Model
Semiconductor energy band model. EC and EV are energy levels at the edge of the conduction and valence bands.
Electron participating in a covalent bond is in a lower energy state in the valence band. This diagram represents 0 K.
What happens as temperature increases?

## Slide 38: Semiconductor Energy Band Model
Semiconductor energy band model. EC and EV are energy levels at the edge of the conduction and valence bands.
Electron participating in a covalent bond is in a lower energy state in the valence band. This diagram represents 0 K.
Thermal energy breaks covalent bonds and moves the electrons up into the conduction band.

## Slide 39: Semiconductor energy bands at room temperature
When enough energy is supplied to the e- sitting at the top of the valance band, e- can make a transition to the bottom of the conduction band.
When electron makes such a transition it leaves behind a missing electron state.
This missing electron state is called as a hole.
Hole behaves as a positive charge carrier.
Magnitude of its charge is the same with that of the electron but with an opposite sign.
Forbidden
energy gap [Eg]
Full
valance
band
Empty
conduction
band
+
e-
+
e-
+
e-
+
e-
energy

## Slide 40: 3-2. Carriers in Semiconductors
Ec
Ev
Eg
0ºK
3ºK
2ºK
4ºK
5ºK
1ºK
6ºK
7ºK
8ºK
9ºK
10ºK
11ºK
12ºK
13ºK
14ºK
300ºK
15ºK
16ºK
17ºK
18ºK
19ºK
20ºK
Electron Hole Pair
E
H
P

## Slide 41: THE SEMICONDUCTOR
With the aid of the band theory we have succeeded in classifying solids into metals, insulators and semiconductors. We are now going to consider semiconductors (technologically the newest class) in more detail

## Slide 42: Semi-conductor concepts
Semiconductors are a group of solids whose electrical properties are intermediate between conductors and insulators. For example, the resistivity of a conductor is of the order of 10-8 m, that of an insulator is 104 m and above whiles that of a semiconductor is 10-1m.
Most semiconductor devices require materials with an energy gap of about 1eV at normal room temperature. Hence, the most extensively used semiconducting elements in the electronic industry are silicon (1.2eV) and germanium (0.76 eV). Silicon and germanium are group IV elements

## Slide 43: Semiconductors
A material whose properties are such that it is not quite a conductor, not quite an insulator
Some common semiconductors
  elemental
    Si - Silicon (most common)
    Ge - Germanium
  compound
    GaAs - Gallium arsenide
    GaP - Gallium phosphide
    AlAs - Aluminum arsenide
    AlP - Aluminum phosphide
    InP - Indium Phosphide

## Slide 44: The name “semiconductor” implies that it conducts somewhere between the two cases (conductors or insulators)
Conductivity :
σmetals ~1010 /Ω-cm
σinsulators ~ 10-22 /Ω-cm
The conductivity (σ) of a
semiconductor (S/C) lies
between these two
extreme cases.
S/C

## Slide 45: Basic Semiconductor Concepts
Intrinsic Semiconductor
Doped Semiconductor

## Slide 46: 3.1: Intrinsic Semiconductors
silicon at low temps:
  all covalent bonds are intact
  no electrons are available for conduction
  conducitivity is zero
silicon at room temp:
  sufficient thermal energy exists to break some covalent bonds, freeing an electron and creating hole
  a free electron may wander from its parent atom
  a hole will attract neighboring electrons
the process of freeing electrons, creating holes, and filling them facilitates current flow
At room temperature, some of the covalent bonds are broken by thermal generation. Each broken bond gives rise to a free electron and a hole, both of which become available for current conduction.

## Slide 47: Intrinsic Semiconductors
thermal generation – effects a equal concentration of free electrons and holes.
  Therefore, electrons move randomly throughout the material.
In thermal equilibrium, generation and recombination rates are equal.
Notes: The holes and electrons are randomly distributed in the material.

## Slide 48: Intrinsic Semiconductors
intrinsic semiconductor – is one which is not doped
  One example is pure silicon.
generation – is the process of free electrons and holes being created.
  generation rate – is speed with which this occurs.
recombination – is the process of free electrons and holes disappearing.
  recombination rate – is speed with which this occurs.
Generation may be effected by thermal energy. As such, both generation and recombination rates will be (at least in part) a function of temperature.
Notes: We are assuming pure Crystalline semiconductors as opposed to amorphous semiconductor materials

## Slide 49: Intrinsic semiconductor

## Slide 50: Electron Distribution
As more energy is applied to a semiconductor, more electrons will move into the conduction band and current will flow more easily through the material.
Therefore, the resistance of intrinsic semiconductor materials decreases with increasing temperature.
This is a negative temperature coefficient.

## Slide 51: Intrinsic carrier concentration in semiconductors
The density of carriers in a semiconductor as a function of temperature and material properties is:
ni = number of free electrons and holes in a unit volume for intrinsic semiconductor
Ns = parameter whose precise value depends on the material
T = temperature (K)
Eg = bandgap energy
k = Boltzman constant
Notes: This is the Fermi-Dirac distribution. See http://DoctorD.webhop.net/Courses/BEI/EE231/supplement1_carrierconc.pdf

## Slide 52: Free Electron Density at a Given Temperature
Eg, or bandgap energy determines how much effort is needed to break off an electron from its covalent bond.
There exists an exponential relationship between the free-electron density and bandgap energy.

## Slide 53: Electron-hole concentrations
A vacancy is left when a covalent bond is broken.
The vacancy is called a hole.
A hole moves when the vacancy is filled by an electron from a nearby broken bond (hole current).
The electron density is n (ni for intrinsic material)
Hole density is represented by p.
For intrinsic silicon, n = ni = p.
The product of electron and hole concentrations is pn = ni2.
The pn product above holds when a semiconductor is in thermal equilibrium (not with an external voltage applied).

## Slide 54: Problem
The problem with intrinsic semiconductors are;
Charge carriers are thermally generated and very few in number resulting in very little current.
Thus for device applications, where an appreciable current is required we need to carry out the “doping process” resulting in extrinsic semiconductors

## Slide 55: Semiconductor Doping
The interesting properties of semiconductors emerges when impurities are introduced.
Doping is the process of adding very small well controlled amounts of impurities into a semiconductor.
Doping enables the control of the resistivity and other properties over a wide range of values.
For silicon, impurities are from columns III and V of the periodic table.

## Slide 56: Doped Semiconductors
lattice
p-type dopants
n-type dopants

## Slide 58: Donor Impurities in Silicon
Phosphorous (or other column V element) atom replaces silicon atom in crystal lattice.
Since phosphorous has five outer shell electrons, there is now an ‘extra’ electron in the structure.
Material is still charge neutral, but very little energy is required to free the electron for conduction since it is not participating in a bond.

## Slide 59: Donor Impurities in Silicon
Phosphorous (or other column V element) atom replaces silicon atom in crystal lattice.
Since phosphorous has five outer shell electrons, there is now an ‘extra’ electron in the structure.
Material is still charge neutral, but very little energy is required to free the electron for conduction since it is not participating in a bond.
A silicon crystal doped by a pentavalent element (f. i. phosphorus). Each dopant atom donates a free electron and is thus called a donor. The doped semiconductor becomes n type.

## Slide 61: Pentavalent Doping

## Slide 62: Acceptor Impurities in Silicon
Boron (column III element) has been added to silicon.
There is now an incomplete bond pair, creating a vacancy for an electron.
Little energy is required to move a nearby electron into the vacancy.
As the ‘hole’ propagates, charge is moved across the silicon.

## Slide 63: Acceptor Impurities in Silicon
Boron (column III element) has been added to silicon.
There is now an incomplete bond pair, creating a vacancy for an electron.
Little energy is required to move a nearby electron into the vacancy.
As the ‘hole’ propagates, charge is moved across the silicon.
A silicon crystal doped with a trivalent impurity (f.i. boron). Each dopant atom gives rise to a hole, and the semiconductor becomes p type.
Vacancy

## Slide 66: Doped Semiconductor
Doped semiconductors are materials in which carriers of one kind predominate.
Only two types of doped semiconductors are available.
Conductivity of doped semiconductor is much greater than the one of intrinsic semiconductor.
The pn junction is formed by doped semiconductor.

## Slide 67: Doped Semiconductor(cont’d)
  Majority carrier is only determined by the impurity, but independent of temperature.
  Minority carrier is strongly affected by temperature.
  If the temperature is high enough, characteristics of doped semiconductor will decline to the one of intrinsic semiconductor.

## Slide 68: Energy Band Model for a Doped Semiconductor
Semiconductor with donor or n-type dopants. The donor atoms have free electrons with energy ED. Since ED is close to EC, (about 0.045 eV for phosphorous), it is easy for electrons in an n-type material to move up into the conduction band.

## Slide 69: Energy Band Model for a Doped Semiconductor
Semiconductor with donor or n-type dopants. The donor atoms have free electrons with energy ED. Since ED is close to EC, (about 0.045 eV for phosphorous), it is easy for electrons in an n-type material to move up into the conduction band and create negative charge carriers.
Semiconductor with acceptor or p-type dopants. The acceptor atoms have unfilled covalent bonds with energy state EA. Since EA is close to EV, (about 0.044 eV for boron), it is easy for electrons in the valence band to move up into the acceptor sites and complete covalent bond pairs, and create holes – positive charge carriers.

## Slide 70: Extrinsic Material
0ºK
3ºK
2ºK
4ºK
5ºK
1ºK
6ºK
7ºK
8ºK
9ºK
10ºK
11ºK
12ºK
13ºK
14ºK
50ºK
15ºK
16ºK
17ºK
18ºK
19ºK
20ºK
Ec
Ev
Ed
Donor
V
P
As
Sb

## Slide 71: Extrinsic Material
ш
B
Al
Ga
In
0ºK
3ºK
2ºK
4ºK
5ºK
1ºK
6ºK
7ºK
8ºK
9ºK
10ºK
11ºK
12ºK
13ºK
14ºK
50ºK
15ºK
16ºK
17ºK
18ºK
19ºK
20ºK
Ec
Ev
Ea
Acceptor

## Slide 72: Hole and Electron Concentrations
To produce reasonable levels of conduction doesn’t require much doping
  silicon has about 5 x 1022 atoms/cm3
  typical dopant levels are about 1015 atoms/cm3
In undoped (intrinsic) silicon, the number of holes and number of free electrons is equal, and their product equals a constant
  actually, ni increases with increasing temperature
This equation holds true for doped silicon as well, so increasing the number of free electrons decreases the number of holes
np = ni2

## Slide 73: Electron and Hole Densities
The product of electron and hole densities is ALWAYS equal to the square of intrinsic electron density regardless of doping levels.
Majority Carriers :
Minority Carriers :
Majority Carriers :
Minority Carriers :

## Slide 74: Questions ?

## Slide 75: pn Junction
The pn junction under open-circuit condition
  Diffusion and Drift currents
The pn junction under closed circuit conditions
  Forward bias
  Reverse bias
I-V characteristic of pn junction
  Terminal characteristic of junction diode.

## Slide 77: Introduction
IN THIS LECTURE WE WILL LEARN:
  The two mechanisms by which current flows in semiconductors – drift and diffusion charge carriers.
  The structure and operation of the pn junction – a basic semiconductor structure that implements the diode and plays a dominant role in semiconductors.

## Slide 78: P-N Junction
Open circuit conditions
The p-n junction possesses some interesting properties which have useful applications in modern electronics. Thus an understanding of the physical operations of p-n junctions is important to the understanding of the operation and terminal characteristics these electronic devices

## Slide 79: P-N JUNCTION FORMATION
Three important phenomena occur during the formation of a P-N Junction namely;
Diffusion
Space charge
Drift

## Slide 81
As
As
As
As
As
B
B
B
B
B
N
P
Formation of the P-N Junction
Covalent bond
Free electron
Hole
Silicon atom
P-N Junction
Electron diffusion
Hole diffusion

## Slide 82
+
+
+
As
As
-
-
-
B
B
N
P
The combining of electrons and holes depletes the holes in the p-region and electrons in the n-region near the junction
Depletion Region/Space Charged Region

## Slide 83
As a result of the barrier pd, an electric field is set up in the depletion region, and it prevent further diffusion of charge carriers across the junction.
+
+
+
As
As
-
-
-
B
B
N
P

## Slide 84: P-N Junction formation
As the free electrons move across the junction from n-type to p-type, +ve donor ions are uncovered. Hence a +ve charge is built on the n-side of the junction. At the same time, the free electrons cross the junction and uncover the –ve acceptor ions by filling in the holes. Therefore a net –ve charge is established on p-side of the junction.

## Slide 85: P-N Junction formation
When a sufficient number of donor and acceptor ions are uncovered further diffusion is prevented.
Thus a barrier is set up against further movement of charge carriers. This is called potential barrier or junction barrier Vo. The potential barrier is of the order of 0.1 to 0.3V.
Note: outside this barrier on each side of the junction, the material is still neutral. Only inside the barrier, there is a +ve charge on n-side and –ve charge on p-side. This region is called depletion layer.

## Slide 86: Drift Current
In addition to the current component, ID, due to majority carrier diffusion, a component due to minority carrier drift exists across the junction.

## Slide 87
If for some reason, ID exceeds Is, then more bound charge will be uncovered on both sides of the junction, the depletion layer will widen and the voltage across it Vo will increase. This in turn causes ID to decrease until equilibrium is achieved with ID = Is.

## Slide 88
On the other hand, if Is exceeds ID, then the amount of uncovered charge will decrease, the depletion layer will narrow and the voltage across it will decrease. This causes ID to increase until equilibrium is achieved with ID = Is

## Slide 89: pn Junction Under Open-Circuit Condition
Fig (a) shows the pn junction with no applied voltage (open-circuited terminals).
Under open circuit conditions, no external current exists; thus the two opposite currents across the junction should be equal in magnitude i.e., ID = Is..

## Slide 90: Summary of Procedure for Forming pn Junction
The procedure of forming pn the dynamic equilibrium of drift and diffusion movements for carriers in the silicon. In detail, there are 4 steps:
  Diffusion
  Space charge region
  Drift
  Equilibrium

## Slide 91: Procedure of Forming pn Junction
diffusion
    Both the majority carriers diffuse across the boundary between p-type and n-type semiconductor.
    The direction of diffusion current is from p side to n side.

## Slide 92
3.7.2 The pn junction Under Open-Circuit Conditions
Diffusion current!
Acceptors (B, III) accept, recombine with electrons and become (-).
Donors (P, IV) donate electrons and become (+).
This process produces electric potential and field and stops when coulomb force equals to diffusion mechanism.
There is no free electron and holes in this region.
This region is depleted of free carriers !!
E field
E field
Drift current!
Minority carriers
Diffusion
0.1~1 μm
0.6~0.8 V
Notes: sedr42021_0345a.jpg

## Slide 94: P-N Junction
Closed circuit conditions

## Slide 95: Forward Biased Junction
An external source can either oppose or aid the barrier potential.
If the positive side of the voltage is connected to the p-type material, and the negative side to the n-type material, then the junction is said to be forward biased.

## Slide 96: P-N Junction in Forward Bias
When the N-type region of a pn junction is at a lower potential than the P-type region, the pn junction is in forward bias.
The depletion width is shortened and the built-in electric field decreased.

## Slide 98: Biasing the Junction (forward)
Now the negative charges are driven toward the junction in the N material and the positive charges also are driven toward the junction in the P material. The depletion zone shrinks and will disappear if the voltage exceeds a threshold. This is called forward bias.

## Slide 99: P-N junction (closed circuit) forward bias
Note that for a forward biased pn junction there is a threshold voltage, below which no current flows across the junction

## Slide 100: Forward Biased Junction
In a forward biased junction, the following conditions exist:
  Forward bias overcomes barrier potential.
  Forward bias narrows the depletion region.
  There is maximum current flow with forward bias.

## Slide 101: Reverse Biased Junction
Reverse bias occurs when the negative source is connected to the p-type material and the positive source is connected to the n-type material.
Reverse bias strengthens the barrier potential.
Reverse bias widens the depletion region.
Current flow is minimum.

## Slide 102: P-N Junction in Reverse Bias
When the N-type region of a pn junction is connected to a higher potential than the P-type region, the pn junction is under reverse bias, which results in wider depletion region and larger built-in electric field across the junction.

## Slide 103: Reverse Biased Junction
A reversed biased junction has zero current flow (ideally).
Reverse current is temperature dependent.
If reverse biased is increased enough, the reverse current increases dramatically.
This breakdown is called junction breakdown. The voltage required to reach this point is the reverse breakdown voltage.
As the breakdown occurs, avalanche may occur and destroy the device if uncontrolled.

## Slide 104: Biasing the Junction (reverse)
Apply a voltage as indicated. The free charge carriers (negative charges in the N material and positive charges in the P material) are attracted to the ends of the crystal. No charge flows across the junction and the depletion zone grows. This is called reverse bias.

## Slide 105
P
N
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
Space charge region
Open circuit PN -junction
-
-
-
-
-
-
-
-
-
-
-
-
+
+
+
+
+
+
+
+
+
+
+
+
P
N
Reverse bias
VR

## Slide 106
The experimental I-V characteristic of a Si diode

## Slide 108
BREAKDOWN REGION
Breakdown occurs when p–n junctions are operated in the reverse-bias mode.
This breakdown occurs at a critical reverse-bias voltage (Vz). At this critical voltage the reverse current through the diode increases sharply, and relatively large currents flow with little increase in voltage.
The following two mechanisms can cause reverse breakdown in a junction diode.

## Slide 109
BREAKDOWN REGION
Zener Breakdown
  Zener breakdown occurs when a sufficiently large reverse-bias is applied across a p–n junction (diode). The resulting electric field at the junction imparts a very large force on a bound electron, enough to dislodge it from its covalent bond.
  The breaking of the covalent bonds produces a large number of EHP (electron–hole pairs). Consequently the reverse current becomes very large. This type of breakdown phenomena is known as Zener breakdown.

## Slide 110
BREAKDOWN REGION
Avalanche Breakdown
  In a reverse-biased junction, the minority-carriers drift across the depletion region. On their way across this region, they occasionally have collisions with atoms in the lattice.
  With a large enough field, a carrier drifting across the depletion region is accelerated to the point where it has enough energy to knock a valance electron free from its host atom during a collision.
  The field then separates the electron and hole of this newly created EHP and we now have three mobile carriers instead of one. This process is called avalanche multiplication.
  The multiplication can become quite large if the carriers generated by this collision also acquire to create more carriers, thereby initiating a chain reaction.
  Once the process starts, the number of multiplication that can occur from a single collision increases rapidly with further increase in the reverse-bias, so the terminal current grows rapidly, and we say that the junction breaks down. This is called avalanche breakdown.

## Slide 111
BREAKDOWN REGION
Avalanche breakdown in low doped semiconductor
A single such event results in multiplication of carriers; the original electron as well as the secondary electron are swept to the n-type semiconductor, while, the generated hole is swept to the p-type semiconductors.
Carrier multiplications in the depletion region due to impact ionization

## Slide 112: Breakdown region
If a pn junction breaks down with Vz < 5 V, the breakdown mechanism is usually the zener effect. Avalanche breakdown occurs when Vz > 7 V.

## Slide 113: EXPLAINING PN JUNCTION FORMATION WITH THE ENERGY BAND DIAGRAM

## Slide 114: PN junction formation
The Fermi energy in a p-type and n-type semiconductor before they are brought together to form a p-n junction

## Slide 115: PN junction formation
The Fermi energy has the same value throughout a system in equilibrium – in the absence of external potentials and in thermodynamic equilibrium, there is no net flow of charge or energy across the boundary between two materials.]

## Slide 116: PN junction formation
The junction potential Vo is what brings the Fermi energies to the same level.
Fermi energy
eVo

## Slide 117: Forward bias
When an external potential, Vext, is applied across a pn junction, the junction is said to be biased. In that case there can be a net flow of charge and energy and the Fermi energies no longer need be the same,

## Slide 118: Forward bias
Contact potential is reduced from |Vo| to |Vo| - |Vext|. In that case there can be a net flow of charge and energy and the Fermi energies no longer need be the same,
Vext
Vo
N –type P-type

## Slide 119: Reverse bias
The magnitude of the junction potential is increased from |Vo| to |Vo| + |Vext|. Thus, both electrons from the n-side and holes from the p-side have an even harder time overcoming the additional barrier.

## Slide 120: Reverse bias
the magnitude of the junction potential is increased from |Vo| to |Vo| + |Vext|. Thus, both electrons from the n-side and holes from the p-side have an even harder time overcoming the additional barrier.
Vo
Vext

## Slide 121
I-V characteristics

## Slide 123: Questions ?

## Slide 124: Procedure of Forming pn Junction
Space charge region
  Majority carriers recombining with minority carriers results in the disappearance of majority carriers.
  Bound charges, which will no longer be neutralized by majority carriers are uncovered.
  There is a region close to the junction that is depleted of majority carriers and contains uncovered bound charges.
  This region is called carrier-depletion region or space charge region.

## Slide 125: Procedure of Forming pn Junction
Drift
  Electric field is established across the space charge region.
  Direction of electronic field is from n side to p side.
  It helps minority carriers drift through the junction. The direction of drift current is from n side to p side.
  It acts as a barrier for majority carriers to diffusion.

## Slide 126: Procedure of Forming pn Junction
Equilibrium
  Two opposite currents across the junction is equal in magnitude.
  No net current flows across the pn junction.
  Equilibrium conduction is maintained by the barrier voltage.