## Slide 1: Dr Emmanuel Ahene
Assembly Language Programming
Beyond basics –L3

## Slide 2: Assembly Basic Syntax/structure
An assembly program can be divided into three sections:
The data section
The bss section
The text section

## Slide 3: Memory Segments
A segmented memory model divides the system memory into groups of independent segments, referenced by pointers located in the segment registers. Each segment is used to contain a specific type of data. One segment is used to contain instruction codes, another segment stores the data elements, and a third segment keeps the program stack.

## Slide 4: Memory Segments
In the light of the above discussion, we can specify various memory segments as:
Data segment - it is represented by .data section and the .bss. The .data section is used to declare the memory region where data elements are stored for the program.
This section cannot be expanded after the data elements are declared, and it remains static throughout the program.

## Slide 5: Memory Segments
  The .bss section is also a static memory section that contains buffers for data to be declared later in the program. This buffer memory is zero-filled.
  Code segment - it is represented by .text section. This defines an area in memory that stores the instruction codes. This is also a fixed area.  Stack - this segment contains data values passed to functions and procedures within the program

## Slide 6: ASSEMBLY REGISTERS
Processor operations mostly involve processing data. This data can be stored in memory and accessed from thereon.
However, reading data from and storing data into memory slows down the processor, as it involves complicated processes of sending the data request across the control bus, and into the memory storage unit and getting the data through the same channel.

## Slide 7: ASSEMBLY REGISTERS
To speed up the processor operations, the processor includes some internal memory storage locations, called registers.
The registers stores data elements for processing without having to access the memory. A limited number of registers are built into the processor chip.

## Slide 8: PROCESSOR REGISTERS
In IA-32 architecture, registers hold 32 bits. This means each
register can hold the values:
Unsigned : 0 to 4294967295
Signed: -2147483648 to 2147483647
In the x86_64 architecture, registers hold 64 bits. This means each
register can hold the values :
Usigned: 0 to 18,446,744,073,709,551,616
Signed: -9,223,372,036,854,775,808 to 9,223,372,036,854,775,807

## Slide 9: Registers
Registers (32/64Bits) are grouped into three categories:
  General registers
  Control registers
  Segment register

## Slide 10: PROCESSOR REGISTERS (32 & 64 bits)
The general registers are further divided into the following groups:
  Data registers
  Pointer registers
  Index registers

## Slide 11
Register Table

## Slide 12: Data Registers (32 bits)
Four 32-bit data registers are used for arithmetic, logical and other operations. These 32-bit registers can be used in three ways:
As complete 32-bit data registers: EAX, EBX,
ECX, EDX.
Lower halves of the 32-bit registers can be used
as four 16-bit data registers: AX, BX, CX and DX.
Lower and higher halves of the above-mentioned
four 16-bit registers can be used as eight 8-bit
data registers: AH, AL, BH, BL, CH, CL, DH, and
DL

## Slide 13: Data Registers (32 bits)

## Slide 14: Data Registers
Some of these data registers has specific used in arithmetical operations.
AX is the primary accumulator; it is used in input/output and most arithmetic instructions.
For example, in multiplication operation, one operand is stored in EAX, or AX or AL register according to the size of the operand.
BX is known as the base register as it could be used in indexed addressing.

## Slide 15: Data Registers
CX is known as the count register as the ECX, CX registers store the loop count in iterative operations. DX is known as the data register. It is also used in input/output operations.
It is also used with AX register along with DX for multiply and divide operations involving large values

## Slide 16: Hello World Source codes
Any differences?

## Slide 17: Hello World into details

## Slide 18: And….

## Slide 19: And….

## Slide 20: Sections onward….

## Slide 21: Labels Onward……

## Slide 22: The “_Start” label

## Slide 23
Global

## Slide 24: Other important ones…

## Slide 25
…System Call

## Slide 26: System call inputs by registers

## Slide 27: System Call List

## Slide 28: Sys_write

## Slide 29
Sys_write

## Slide 30
Sys_write

## Slide 31: Sys_write

## Slide 32: Sys_write

## Slide 33
Sys_write

## Slide 34
Sys_exit

## Slide 35
The pointer registers are 32-bit EIP, ESP and EBP registers and corresponding 16-bit right portions IP, SP and BP. There are three categories of pointer registers:
Instruction Pointer (IP) - the 16-bit IP register stores the offset address of the next instruction to be executed. IP in association with the CS register (as CS:IP) gives the complete address of the current instruction in the code segment.
Pointer Registers

## Slide 36
Hello_world.asm ;
display hello world on the screen
Addition.asm / Subtraction.asm ;
add/subtract two numbers and display the answer to screen
Compare.asm ;
compare 3 numbers and display the greatest on screen
See WhatsApp group for sample codes
Assignment:
Write the compare.asm code in 64 bits.
To be submitted on 3/06/2021
Sample programs done: